## Slide 1
Structure machine
Ch1. Introduction to digital systems

## Slide 2
1. Basic Logical Operations
Presentation plan
2. Basic Logic Functions
3. Integrated circuits (IC)
3.1. Integrated circuit (CI)
3.2. IC packages (classification according to the principle of mounting on printed circuit board)
3.3. Pin numbering
3.4. IC Complexity Classification (continued)
3.5. IC Technologies

## Slide 3
1. Basic Logical Operations
A proposition and the conditions
If "The bulb is not burned out" and "The switch is on"  "The light is on"
Logic (the field of human reasoning that determines whether a given proposition is true or false (when certain conditions are true))
A proposition can be true or false.
Combination of several propositions  A logical function
George Boole (1850)  Boolean Algebra

## Slide 4
Digital circuit used in the implementation of logic functions  Logic circuit
1. Basic Logical Operations (continued)
Logic circuits  Digital system (computer)
Basic Logical Operations ( logical function)
  NOT
  AND
  OR
Standard symbols for basic logical operations

## Slide 5
Circuit that performs a specific logical operation  Logic gate (NOT gate,
AND gate, OR gate)
  True Input (True Condition)  HIGH level
  False input (false condition)  LOW level
Logical operation NOT  Inverter (logic gate)
1. Basic Logical Operations (continued)

## Slide 6
Logical operation AND  AND gate (logic gate)
Logical OR operation  OR gate (logic gate)
1. Basic Logical Operations (continued)

## Slide 7
2. Basic Logic Functions
Combination of logic gates  Complex logic circuit
Combination of basic logical operations ( Logic Function)
Basic Logic Functions
  Comparison
  Arithmetic
  Code conversion
  Coding
  Decoding
  Data selection
  Storage
  Counting

## Slide 8
2. Basic Logic Functions (Comparison)
Comparison  Comparator

## Slide 9
Addition Adder
2. Basic Logic Functions (Arithmetic functions)

## Slide 10
Subtraction  Subtractor
Nombre binaire
Nombre binaire
A
B
Entrée d’emprunt
Différence
Sortie d’emprunt
2. Basic Logic Functions (Arithmetic functions) (continued)

## Slide 11
Multiplication  Multiplier
Binary number
Binary number
A
B
Product
Multiplication = Addition + Product Position Shift  Multiplication can be done
by an adder + other circuits
Division = Subtraction + Comparison + Shift  Division can be performed by a subtractor + other circuits
Division  Divisor (2 inputs and 2 outputs (quotient + remainder))
2. Basic Logic Functions (Arithmetic functions) (continued)

## Slide 12
2. Basic Logic Functions (Coding)
Coding (conversion of information (decimal number or alphabet character) into coded form (binary))  Encoder

## Slide 13
2. Basic logic functions (decoding)
Decoding  decoder (conversion of coded (binary) information into uncoded form)
Decoder performing the conversion of a binary code on a seven-segment display

## Slide 14
2. Basic Logical Functions (Data Selection)
Data selection  Multiplexer and demultiplexer
Multiplexer (multiple inputs  output) (like an electronic switch sequentially connecting each of the input lines to the output line)
Demultiplexer (one input  multiple output lines according to a specific timeline)
Multiplexer and demultiplexer Remote data transmission

## Slide 15
Time Division Multiplexing
2. Basic Logical Functions (Data Selection) (continued)

## Slide 16
2. Basic Logical Functions (Data Storage)
Storage  storage unit
Flip-flop (bistable logic circuit whose output indicates which bit is currently stored)
(Shift) Register (Flip-Flops Combinations)  Storing a group of bits
Shifting bits (from one position to another)
(Shift) Register (Flip-Flops Combinations)  Shifting bits (from one position to another)
Serial Shift Register
Parallel shift register

## Slide 17
4. Basic Logical Functions (Data Storage (continued))
Semiconductor memories (storage of large quantities of bits) Mémoire morte (ROM)
  Random Access Memory (RAM)
  Cache memory (cache or buffer memory)
  Semiconductor flip-flop
  Register that consists of semiconductor flip-flops
Magnetic memories  Mass storage of binary data
  Hard disk
  Optical disc (It uses laser beams to store and retrieve data)
  Magnetic tape

## Slide 18
2. Basic Logic Functions (Counting)
Counting  Counter (count events)
A counter is composed of a memory (based on flip-flops)

## Slide 19
3. Integrated circuits (IC)
Integrated circuit (IC) (electronic circuit built entirely on a single Si chip)
IC (advantages)
  Size
  Reliability
  Cost
  Consumption (electrical)
Cutaway view of a typical IC package
showing the chip mounting
and connections to the input and output pins
3.1. Integrated circuit (IC)

## Slide 20
3. Integrated circuits (IC) (continued)
3.2. IC packages (classification according to the principle of mounting on printed circuit board)
Insertion Mount Integrated Circuits
Dual In-Line Package (DIP)
Surface-Mount Technology (SMT) Integrated Circuits

## Slide 21
3.3. Pin numbering
DIP + SOIC + FP
PLCC + LCCC
3. Integrated circuits (IC) (continued)

## Slide 22
3. Integrated circuits (IC) (continued)
3.4. IC complexity classification
Small Scale Integration (SSI) (number of equivalent logic gates < 12)
  Basic Logic Gates
  Toggles
Medium-scale integration (MSI) (12 ≤ number of equivalent logic gates ≤ 99)
  Coders
  Decoders
  Counters
  Registers
  Multiplexer
  Arithmetic circuits
  Little memories

## Slide 23
3.4. IC complexity classification (continued)
Large Scale Integration (LSI) (100 ≤ number of equivalent logic gates ≤ 9999)
  Memories
Very Large Scale Integration (Very LSI (VLSI)) (10000 ≤ number of equivalent logic gates ≤ 99999)
Ultra-large scale integration (Ultra LSI) (number of equivalent logic gates ≥ 100000)
  Very large memory
  Powerful microprocessors
3. Integrated circuits (IC) (continued)

## Slide 24
3. Integrated circuits (IC) (continued)
3.5. IC Technologies
Bipolar Transistor Based IC Technologies
  TTL (Transistor-Transistor Logic)
  ECL (Emitter Coupled Logic)
SC-Metal-Oxide Field-Effect Transistor (MOSFET) Technology
  CMOS (complementary MOS)
  NMOS (MOS) N channel
TTL Technology  SSI and MSI
CMOS or NMOS  SSI and MSI and LSI and VLSI and ULSI