## Slide 1
Structure machine 2
Ch3. Sequential logic
(Part 3-1)

## Slide 2
1.1. S-R bistable
Presentation plan of chapter 3
1. Bistable
1.2. S-R bistable with validation input
1.3. D bistable
2.1. Horloge temps réel ou RTC (Real Time Clock) (rappels)
2. Flip-flops triggered by a positive or negative edge
2.2. Introduction to Clock-Triggered Flip-Flops
2.3. S-R Clock-triggered flip-flop
2.4. D Clock-triggered flip-flop
2.5. J-K Clock-triggered flip-flop
2.6. Asynchronous inputs
3. Toggle applications

## Slide 3
1.1. S-R bistable
1. Bistables
bistable with LOW valid state input
Q = 1 (output that corresponds to )  The bistable is in state 1 (SET)
Q = 0 (output that corresponds to )  The bistable is in state 0 (RESET)
Truth table of bistable with LOW valid state input

## Slide 4
1.1. S-R bistable (following)
Logic symbol of bistable with LOW valid state input

## Slide 5
1.2. S-R bistable with validation input
Logic diagram of
S-R bistable with validation input
VAL | S | R | Qn | Q̅n
0 | X | X | Qn-1 | Q̅n-1
1 | 0 | 0 | Qn-1 | Q̅n-1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 |  | 
Condition non valide
S-R bistable with validation input
  VAL = 1  Q = f(S,R) et Q̅ = f(S,R) as in a S-R bistable with a valid HIGH state input
  VAL = 0  Q and Q̅ do not change
Truth table of
S-R bistable with validation input

## Slide 6
1.2. S-R bistable with validation input (following)
Logic symbol of S-R bistable with validation input

## Slide 7
1.3. D Bistable
D bistable is a type of bistable with validation input.
Logic diagram of D bistable (D for data)
VAL | D | Qn | Q̅n
0 | X | Qn-1 | Q̅n-1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Truth table of D bistable
Bistable D
  VAL = 1  Q = D (Q follows D input)
  VAL = 0  Q et Q̅ do not change

## Slide 8
1.3. D Bistable (following)
Logic symbol of D bistable