## Slide 1
Seismic Engineering
Génie parasismique (Master2 G.C)

Responsible: Dr. GUETTICHE ABDELHEQ

Academic Year: 2024- 2025
UNIVERSITY CENTER OF MILA
INSTITUTE OF SCIENCE AND TECHNOLOGY DEPARTMENT OF CIVIL AND HYDRAULIC ENGINEERING
Chapter 6. Modal Spectral Dynamic Method

## Slide 2
Voir RPA 2024 (Pages: 78 - 80) 1. Principle : With this method, for each vibration mode, the maximum effects generated in the structure by the seismic forces represented by a design response spectrum are sought. These effects are then combined to obtain the response of the structure.
The assumed elastic behavior of the structure allows the calculation of natural modes.
2. Modeling :
a) For regular structures in plan with rigid floors, the analysis is done separately in each of the two main directions of the building. The latter is then represented in each of the two calculation directions by a planar model, fixed at the base and where the masses are concentrated at the level of the centers of gravity of the floors with a single DOF in horizontal translation.
b) For irregular structures in plan, subject to torsion and with rigid floors, they are represented by a three-dimensional model, fixed at the base and where the masses are concentrated at the level of the centers of gravity of the floors with three (03) DOF (2 horizontal translations and one vertical axis rotation).
c) For regular or non-regular structures with flexible floors, they are represented by three-dimensional models fixed at the base and with multiple DOF per floor..

## Slide 3
d) The deformability of the foundation soil must be taken into account in the model whenever the response of the structure depends significantly on it.
e) The building model to be used must best represent the distributions of stiffnesses and masses in order to take into account all significant deformation modes in the calculation of seismic inertial forces (contribution of nodal zones and non-structural elements to building stiffness).
f) In the case of reinforced concrete or masonry buildings, the stiffness of the load-bearing elements must be calculated considering the uncracked sections. If displacements are critical, especially in the case of structures associated with high behavior coefficient values, a more precise estimate of stiffness becomes necessary by taking into account cracked sections.
3. Number of modes to consider:
For structures represented by planar models in two orthogonal directions, the number of vibration modes to be retained in each of the two directions of excitation must be such that:
the sum of the effective modal masses for the retained modes is equal to at least 90% of the total mass of the structure.
or that all modes having an effective modal mass greater than 5% of the total mass of the structure are retained for determining the total response of the structure. The minimum number of modes to be retained is three (03) in each direction considered.

## Slide 4
the first two modes must verify translation along the two orthogonal axes (x, y), and torsion for the third mode.
In cases where the conditions described above cannot be satisfied due to the significant influence of torsional modes, the minimum number of modes (K) to be retained must be such that:
where:
N is the number of levels above ground
Tk is the period of mode K
4.Design spectrum:
To avoid an explicit nonlinear structural analysis during calculations, the structure's capacity to dissipate energy, primarily through its ductile behavior, is taken into account by performing an elastic analysis based on a response spectrum reduced compared to the elastic one, referred to as the design spectrum.
This reduction is achieved by introducing a reduction factor for elastic forces, known as the behavior coefficient (R), along with a penalty factor called the quality factor (QF).
The horizontal seismic action is represented by the following design spectrum:

## Slide 5
Design spectrum normalized with respect to the value of gravitational acceleration, g.
R: behavior coefficient of the structure
• QF: Quality factor (see § 3.8).
A: Design acceleration coefficient for a class S1 soil for return period of Tr = 475 years.
I: Importance coefficient; S: Site coefficient.
T1: Lower limit of the periods corresponding to the plateau of constant spectral acceleration;
T2: Upper limit of the periods corresponding to the plateau of constant spectral acceleration;
T3: Value defining the beginning of the branch with constant spectral displacement.
η: Damping correction coefficient.
The values of the periods T1 and T2, as well as the site coefficient S, which define the shape of the elastic response spectrum, depend on the level of seismicity and the soil class.

## Slide 6
4.1Values of parameters describing the design spectra
Two types of spectrum shapes are used:Type 1 and Type 2bdepending on the seismic zone:
Type 1: Applied to seismic zones IV, V, and VI
Type 2: Applied to seismic zones I, II, and III
For the four soil classes S1, S2, S3, and S4, the recommended values for the parameters S, T1, T2, and T3 are provided in:Table (3.3) for the Type 1 spectrum Table (3.4) for the Type 2 spectrum. Figure (3.3) shows the shapes of the Type 1 and Type 2 spectra for 5% damping and normalized by A.
Spectrum Type 1(Zones IV, V & VI) | S | T1 (s) | T2 (s) | T3 (s)
site: S1 | 1.00 | 0.10 | 0.40 | 2.0
site: S2 | 1.20 | 0.10 | 0.50 | 2.0
site: S3 | 1.30 | 0.15 | 0.60 | 2.0
site: S4 | 1.35 | 0.15 | 0.70 | 2.0
Spectum Type 1(Zones I, II & III) | S | T1 (s) | T2 (s) | T3 (s)
site: S1 | 1.00 | 0.05 | 0.25 | 1.20
site: S2 | 1.30 | 0.05 | 0.30 | 1.20
site: S3 | 1.55 | 0.10 | 0.40 | 1.20
site: S4 | 1.80 | 0.10 | 0.50 | 1.20

## Slide 7
-Viscous damping correction coefficient ‘η ’
The value of the viscous damping correction coefficient, η, can be determined by Eqn. (3.9):
Where: ξ(%) is the percentage of critical damping, which depends on the constitutive material, the type of structure, and the extent of infill (see Table (3.5)). When ξ = 5%, we have η = 1.The value of the importance coefficient, I, depends on the importance group (see § 3.4, Table (3.10) & Appendix I).
-Importance coefficient
 | Frame (*) | walls (**)
infill | RC Steel | RC/masonry walls
Light | 6 4 | 10
Dense | 7 5 | 10
(*): Without the presence of shear walls or reinforced concrete cores (**): Values applicable even if the shear walls are combined with frames |  | 
importance coefficient | 1A | 1B | 2 | 3
I | 1.0 | 1.20 | 1 | 0.80

## Slide 8
-Acceleration coefficient:The national territory is divided into seven (07) seismic zones. Each zone is associated with an average acceleration coefficient, serving as a reference value for soil class S1, with a return period of Tr = 475 years, called the zone reference acceleration coefficient (A) (see Table (3.2)).
- Quality factor:
The quality factor, QF, takes into account: • the redundancy and geometry of the elements that constitute the structure • the regularity in plan and elevation The value of QF is determined by Eqn. (3.23):
where: 𝑃q​ is the weighting to be used depending on whether the quality criterion q is 'satisfied or not.' Its value is provided case by case in Table (3.18). •
𝑖: is the total number of weightings depending on the relevant category.
Seismicity Zone | Seismicity Level | A
0 | Very low | -
I | low | 0.07
II | Low to medium | 0.10
III | Medium | 0.15
IV | Medium to high | 0.20
V | high | 0.25
VI | high | 0.30

## Slide 9
The quality criteria 'q' to be verified are:
Comment:
The quality factor, QF, therefore adjusts the value of the behavior coefficient, R, based on the ductility of the bracing system, which is largely controlled by plan and elevation regularities on the one hand, and by the redundancies in resistances (hyperstaticity) in both horizontal directions on the other hand. As a result, the actual behavior coefficient is (R/QF).
Category Criterion, q Observed N/observed |  | 
Plan regularity 2. Elevation regularity 3. Minimum conditions on the number of floors 4. Minimum conditions on the number of spans | 0 | 0.05
 | 0 | 0.20
 | 0 | 0.20
 | 0 | 0.10
Plan regularity Elevation regularity Plan redundancy | 0 | 0.05
 | 0 | 0.20
 | 0 | 0.05
(b)

## Slide 10
Case | Description of the bracing system (see Chapter III, Section 3.6) | Value of R
A 1 2 3 4 5 6 7 8 9 | Reinforced concrete Frame system Mixed bracing system, equivalent to a frame Frame system or mixed system equivalent to a frame with rigid masonry infill Mixed bracing system, equivalent to shear walls Bracing system consisting of shear walls Frame system with core or core effect System operating as a vertical cantilever with predominantly distributed masses Inverted pendulum system Large shear wall system made of lightly reinforced concrete | 5,5 (a) 5,5 (a) 3,5(a) 4,5(b) 4,5(b) 3(b) 3(b) 2(c) 1.5(c)
B 10 11 12a 12b 13a 13b 14 | Steel Frame structures without infill or with isolated infill Frame structures with rigid masonry infill Frame structure with X-centered bracing panels Frame structure with V-centered bracing panels Frame structure with X-centered bracing panels in the form of portals Frame structure with V-centered bracing panels in the form of portals Inverted pendulum system | 6,5 (a) 3(a) 4(b) 2,5(b) 4,5(b) 3,5(b) 2(b)
C 15 16 | Structures incorporating cold-formed profiles (CFP) Bracing system with cold-formed profile (CFP) panels Bracing system with CFP, using tensioned diagonal | 2(b) 1.5(c)
D 17 | Masonry structures Reinforced load-bearing masonry structures | 2,5(b)
F 22 23 24 25 26 | Other systems Metal frame structure with diaphragm bracing Metal frame structure with bracing by core or core effect in reinforced concrete Metal frame structure with bracing by reinforced concrete shear walls Metal frame structure with mixed bracing consisting of a reinforced concrete core and metal bracing panels on the perimeter Metal frame structure with mixed bracing consisting of a reinforced concrete core and metal frames on the perimeter | 2(b) 2.5(b) 3,5(b) 2.5(b) 3,5(b)

## Slide 11
5. Number of modes to consider:
For structures represented by planar models in two orthogonal directions, the number of vibration modes to be retained in each of the two directions of excitation must be such that:
the sum of the effective modal masses for the retained modes is equal to at least 90% of the total mass of the structure.
or that all modes having an effective modal mass greater than 5% of the total mass of the structure are retained for determining the total response of the structure. The minimum number of modes to be retained is three (03) in each direction considered.
the first two modes must verify translation along the two orthogonal axes (x, y), and torsion for the third mode.
In cases where the conditions described above cannot be satisfied due to the significant influence of torsional modes, the minimum number of modes (K) to be retained must be such that:
where: N is the number of levels above ground and Tk is the period of mode K

## Slide 12
6. Combinaison des réponses modales :
In the case where all the retained modal responses are independent of each other, the total response is given by Eqn. (4.11)
b) In the case where all retained modal responses are independent of each other, the total response is given by:
where: E: effect of the considered seismic action
Ei: modal value of E, according to mode 'i’
k: Number of retained modes
c) In the case where two modal responses are not independent; E1 and E2 for example, the total response is given by:
with the correlation factor:
with :
ξ: A single value of the critical damping percentage retained for all the considered modes

## Slide 13
7. Resultant of design seismic forces:
The resultant of the seismic forces at the base Vt obtained by combining the modal values must not be less than 80% of the resultant of the seismic forces determined by the equivalent static method V for a value of the fundamental period given by the appropriate empirical formula. If Vt < 0.80 V, all the response parameters (forces, displacements, moments, ...) must be increased in the ratio 0.8 V/Vt.
8. Effects of accidental torsion:
When an analysis is carried out using planar models in two orthogonal directions, the effects of accidental torsion about the vertical axis must be taken into account as described in paragraph 4.2. 7 (RPA)
In the case where a three-dimensional analysis is carried out, in addition to the calculated theoretical eccentricity, an accidental eccentricity (additional) equal to 0.05 L, (L being the dimension of the floor perpendicular to the direction of the seismic action) must be applied at the level of the floor considered and in each direction.

## Slide 14
9. Common requirements for the "static" and "dynamic" methods:
9.1. Overturning stability: The overturning moment that can be caused by the seismic action must be calculated with respect to the soil-foundation contact level. The stabilizing moment will be calculated taking into account the total weight equivalent to the weight of the construction, the weight of the foundations and possibly the weight of the backfill.
9.2. Vertical component of seismic action: When performing an analysis using planar models in both orthogonal directions, the effects of accidental vertical-axis torsion must be taken into account as described in § 4.2.7. In the case of a three-dimensional analysis, in addition to the calculated theoretical eccentricity, an accidental (additional) eccentricity equal to (±0.05L), where L is the dimension of the floor perpendicular to the direction of the seismic action, must be applied at the level of the considered floor in each direction.
9.3.Calculation of displacements: The horizontal displacement, at each level 'k' of the structure, is calculated according to Eqn. (4.15):Let me know if you'd like to continue:
.
where: 𝛿𝑒𝑘 : Elastic displacement due to seismic forces 𝐹𝑖 (including the torsion effect): Behavior coefficient. 𝑄𝐹: Quality factor
The relative displacement at level 'k' with respect to level 'k −1' is equal to:

## Slide 15
7.4. Displacement calculation: