Supercritical Fluids
 Properties of Supercritical Fluids
Industrial Applications of Supercritical Fluids
 Advantages and Limitations
 Applications in Sustainable Chemistry

---
 Introduction:
Supercritical fluids (SCFs) are substances that are maintained above their critical
temperature (Tc) and critical pressure (Pc), where they exhibit unique properties intermediate between liquids and gases.
In the supercritical state, fluids have liquid-like densities, gas-like viscosities, and very high diffusivities, making them highly efficient solvents in extraction, separation, purification, and chemical reactions.

---
PROPERTIES OF SUPERCRITICAL FLUIDS:
   Density
    -Comparable to liquids
    -Ensures good solvating power
    -Easily adjustable by changing pressure or temperature
   Viscosity
     -Much lower than liquids
     -Facilitates rapid mass transfer
   Diffusivity
    -Higher than liquids
    -Allows the fluid to penetrate solid matrices easily
   Tunable Solvent Power
    -A small change in pressure or temperature can significantly modify solubility
    -Enables controlled extraction and selective separations
    Zero Surface Tension
     -Enhances the ability to diffuse through microporous materials

---
EXAMPLES OF SUPERCRITICAL FLUID
Supercritical Water
Supercritical CO₂
Supercritical Fluorocarbons
Supercritical Methanol and Ethanol

---
Examples of Supercritical Fluids
Supercritical CO₂
Most widely used
Critical point: 31.1°C, 73.8 bars
Non-toxic, non-flammable, cheap
Supercritical Water
Critical point: 374°C, 221 bars
Useful for oxidation, waste destruction, and chemical reactions
Supercritical Fluorocarbons
Used in electronics and fine chemical processing
Supercritical Methanol and Ethanol
Applied in biodiesel production (transesterification without catalysts)

---
Industrial Applications of Supercritical Fluids
Food and Beverage Industry Decaffeination of coffee and tea using SC-CO₂
PharParticlemaceutical Industry size reduction
Petrochemical and Energy Sector extraction of hydrocarbons
Environmental Engineering Green solvents replacing toxic organic solvents

---
Advantages of Supercritical Fluids
Environmentally Friendly
SC-CO₂ is non-toxic, non-flammable, abundant, and cheap
Reduces or eliminates harmful organic solvents
High Selectivity and Efficiency
Adjustable solvent power
Fast diffusion leads to accelerated processes
Low Operating Temperatures
Ideal for thermally sensitive compounds (e.g., vitamins, essential oils)
Quality Improvement
Enhanced purity
No solvent residues in final products
Sustainable and Recyclable
CO₂ can be recycled and reused
Reduces industrial waste

---
 Limitations and Challenges :
High Equipment Cost
Requires high-pressure vessels
Expensive installation and maintenance
Limited Solubility for Polar Compounds
SC-CO₂ is non-polar
Sometimes requires co-solvents (ethanol, methanol)
Operation Complexity
Requires trained personnel
Sophisticated control systems needed
High Pressure Requirements
Safety concerns in industrial settings

---
 Importance of Supercritical Fluids in Green Chemistry
1. Replacement of Organic Solvents
2. Reduction of Waste
3. Energy Efficiency
4. Cleaner Manufacturing Processes
5. High-Purity Products Without Residual Solvents

---
Application in Sustainable Chemistry
 Green Extraction Processes
 Green Synthesis
 Supercritical Water Oxidation (SCWO)
 Biodiesel Production
 CO₂ Utilization Technologies

---
CONCLUSION: Supercritical fluids represent a revolutionary advancement in modern chemical and industrial processes. Their unique physicochemical properties—high diffusivity, adjustable density, low viscosity, and excellent solvation—make them versatile tools in extraction, purification, material processing, and chemical reactions.
Supercritical CO₂ has become a cornerstone of green chemistry, offering a sustainable alternative to traditional solvents with reduced environmental impact.