## Slide 1
Presented by:
ATMA RACHA
SOUIOUAT AMANI
REACTORS
MULTI-FUNCTION
University Abdelhafid boussouf-mila/2025

## Slide 2
Advantages
8.
Objectives
4.
Practical Application
7.
3.
Working Principle
6.
Introduction
Type of Multification Reactors
5.
Overview
  9
conclusion

## Slide 3
Reactors are essential units in chemical engineering for converting raw materials into useful products. Multi-function reactors perform more than one operation at the same time, such as reaction and separation, or reaction and heat transfer. This reduces energy consumption, minimizes waste, and improves process efficiency, in line with the principles of Green Chemistry (Chime Verte). This study focuses on understanding their types, working principle, applications, advantages, and challenges.
Introduction

## Slide 4
  1. Understand the basic principles of multi-function reactors
  2. Identify different types and their characteristics
  3. Study their applications in various industries
  4. Analyze the advantages and challenges
Objective
2025/2026

## Slide 5
Reactive Absorption merges chemical reactions with gas absorption in a liquid. Harmful gases like CO₂ or SO₂ react directly with the absorbing liquid, allowing efficient purification. It is widely used in gas treatment and industrial gas purification processes.
  Reactive absorption:
A reactor that combines chemical reaction + distillation in a single unit. Lighter components rise to the top as a pure product, while heavier components remain at the bottom as by-products or waste, increasing efficiency and saving energy. Used in the production of alcohols and esters.
  Reactive Distillation:
Type of Multifunctional Reactors:
2025/2026

## Slide 6
Reactive Adsorption combines chemical reaction with adsorption on a solid surface such as activated carbon or zeolite. The surface absorbs the reactants while facilitating the reaction. Effective for pollutant removal, gas purification, and surface reactions.
  Reactive adsorption :
Reactive Extraction integrates chemical reaction and separation using a solvent. Substances react and separate simultaneously without high temperatures. Useful in pharmaceutical and food industries, and for isolating organic acids.
  Reactive Extraction:
2025/2026/

## Slide 7
  Combines two or more operations in a single unit, such as a chemical reaction + an additional process (distillation, absorption, adsorption, or extraction) •
  Removes products as they form, increasing chemical conversion efficiency and reducing accumulation of unwanted materials •
  Precise control of temperature, pressure, and material flow ensures continuous reaction and optimal performance •
  Enhances reactor productivity and reduces energy and equipment consumption compared to separate operations •
  Widely used in chemical, pharmaceutical, and energy industries for more efficient and sustainable processes
Working Principle
2025/2026

## Slide 8
  Chemical Industry: Producing chemicals like alcohols, esters, and ammonia; combines reaction + separation in one unit.
  Pharmaceutical Industry: Enables continuous reactions and product separation; essential for drug manufacturing
  Energy & Material Conversion: Applied in gas treatment, hydrogen production, and biofuel processing; reduces energy consumption
  Environmental Applications: Removes pollutants or captures CO₂ from industrial gases; supports cleaner and sustainable processes
Practical Application
2025/2026

## Slide 9
  Saves time, energy, and equipment
  Increases production efficiency
  Integrates multiple processes in a single reactor
  Improves product control and quality
  Reduces operational costs
Advantages
2025/2026

## Slide 10
Multifunctional reactors represent a major advancement in chemical engineering by integrating multiple processes within a single unit. This integration enhances production efficiency, reduces equipment and energy usage, and improves control over product quality. Although they present challenges such as complex design and high initial costs, their advantages make them highly valuable in chemical, pharmaceutical, and energy industries. Ongoing research and development can further optimize their performance and broaden their applications, supporting more sustainable and efficient industrial process
Conclusion
P2025/2026

## Slide 11
Presented by:
ATMA RACHA
SOUIOUAT AMANI
THANK YOU
University Abdelhafid boussouf-mila/2025