## Slide 1
People’s Democratic Republic of Algeria
Ministry of Higher Education and Scientific Research
Abdelhafid Boussouf University-Mila
Institute of Science and Tecnology
Specialization Chemical Engineering
Students:
- Rouimel Hadil
- Belemnigher Houria
Under the supervision of:
- Dr. Mayouf Imane
Ultrasounds In Processes Engineering

## Slide 2
Plan
Introduction
Fundamental Principles of Ultrasounds
Applications of Ultrasounds in Process Engineering
Advantages and Limitations of Ultrasound
The relation between Ultrasounds and Green Chemistry
Conclusion
2
1
3
4
5
6

## Slide 3
1.Introduction:
  Ultrasounds are one of the modern technologies that have revolutionized process engineering in chemical and industrial fields. They rely on the propagation of high frequency mechanical waves (above 20 kHz) through materials, generating a phenomenon known as acoustic cavitation, where microscopic bubbles form, grow, and collapse, releasing high amounts of energy.
  This energy accelerates many chemical and physical processes without the need for high temperatures or hazardous additional substances, making ultrasounds a key tool in green chemistry.

## Slide 4
2.1 Acoustic Cavitation:
Ultrasounds wavens pass through a liquid
The formation of micro-scopic bubbles
The bubbles grow due to pressure changes
Collapse of these bubbles
The collapse generate:
Extremely high local temperatures (up to 5000°C)
High pressures (above 1000 bar)
Shock waves and shear forces
It generates high energy, which is the basis for most industrial applications
2.Fundamental Principles of Ultrasounds:

## Slide 5
2.2 Effects on Chemical Systems:
Increase of the contact surface between materials
Improvement of mass transfer
Fragmentation of solid particles
Acceleration of reactions without additional catalysts

## Slide 6
1/ Ultrasonic Extraction:
2/ Ultrasonic-Assisted Chemical Analysis:
3/
Sonochemistry
4/ Ultrasonic Milling:
5/ Wastewater Treatment:
6/ Medical Applications:
Used to extract natural compounds (essential oils, polyphenols, bioactive molecules).
Increases efficiency while reducing solvent consumption and processing time.
Facilitates sample degradation and preparation.
Shortens pre-analysis steps significantly.
Accelerates many reactions: esterification, hydrolysis, oxidation, etc.
Improves yield and reduces reaction time.
Reduces particle size to the nano-scale.
Important in pharmaceutical and advanced material industries.
Breaks down organic pollutants.
Enhances disinfection and purification processes.
Pain relief and improved blood circulation in physical therapy.
Kidney stone fragmentation ,where high-energy ultrasound waves break stones without surgery.
3.Applications of Ultrasounds in Process Engineering:

## Slide 7
4.The relation between Ultrasounds and Green Chemistry:
Ultrasounds are considered a clean and sustainable technology because they directly support several principles of green chemistry:
Reduction of Solvent Use:
- Ultrasonic extraction requires less solvent than traditional methods.
- In some cases, solvents are not required at all.
Improved Energy Efficiency:
- Faster reactions reduce both time and operational temperatures → less energy consumption.
Reduction of Chemical Waste:
- No need for additional catalysts or reagents.
- Fewer unwanted by-products.
Environmentally Friendly Processes:
- Suitable for food, pharmaceutical, and natural product industries without harmful chemicals.
- Useful in wastewater treatment for eco-friendly pollutant removal.
Enhanced Chemical Safety:
- Many processes occur at moderate temperatures and ambient conditions.
- Less risk compared to traditional high-temperature or high-pressure methods.

## Slide 8
Advantages:
Limitations:
Environmentally friendly (Green).
Significantly faster reaction rates.
Reduced energy and solvent consumption.
Higher product yields.
Accurate and controllable operational conditions.
Uncontrolled heat generation requires temperature regulation.
Scale-up challenges (industrial-scale reactors).
High equipment cost.
5.Advantages and Limitations of Ultrasound :

## Slide 9
6.Conclusion:
  Ultrasounds represent an efficient, modern, and environmentally friendly technology in process engineering. They improve chemical reactions and industrial operations while supporting the key principles of green chemistry by reducing solvent use, improving energy efficiency, and minimizing chemical waste.
  With technological advancements, ultrasound-based processes are expected to become even more important in chemical pharmaceutical, and food industries due to their ability to combine high efficiency with environmental sustainability.