## Slide 1
People's Democratic Republic of Algeria
Ministry of Higher Education and Scientific Research
Faculty of Science and Technology
Department of Process Engineering
2025-2026
Research about :
Prepared by : Khallef Mouaadh-Beniaich Sidali
Use of catalysis in sustainable chemistry
Dr :Mayouf Imane
/

## Slide 2: Use of catalysis in sustainable chemistry

## Slide 3: 01. 03. Table of contents 02. 04.
Definition
Role of Catalysis in Sustainable Chemistry
types of catalysis
Industrial application of Catalysis
Future prospects of catalysis in sustainable development
05.
06.
Conclusion

## Slide 4: Definition 01

## Slide 5
Catalysis plays a crucial role in achieving the goals of sustainable chemistry, as it involves the use of substances called catalysts that lower the activation energy of chemical reactions and provide alternative, more efficient reaction pathways without being consumed in the process. This principle allows reactions to occur under moderate temperature and pressure conditions, thereby reducing energy consumption and minimizing the generation of waste and undesired by-products. By improving chemical selectivity and increasing reaction yields, catalysis contributes to decreasing the environmental footprint of industrial processes and developing cleaner techniques for producing chemicals, fuels, and pharmaceuticals. Moreover, it enables the conversion of low-value raw materials, such as carbon dioxide and biomass, into high-value products, promoting the concept of a circular economy and supporting more sustainable and environmentally friendly production systems.

## Slide 6: types of catalysis
02

## Slide 7
Catalysis is the process of accelerating a chemical reaction using a substance (catalyst) that is not consumed during the reaction.Catalysis is not a single type; rather, there are three main categories relied upon by scientists and industry. Each type has its own characteristics, advantages, disadvantages, and applications.
1. Homogeneous Catalysis
This type of catalysis occurs when all the substances involved in the reaction (reactants + catalyst) are in the same phase, which is often the liquid phase.
Example:If the reaction takes place in an aqueous or alcoholic solution, the catalyst is dissolved in the same solution.
Examples of homogeneous catalysis:
Acids (such as H₂SO₄) as catalysts in esterification reactions.
Metal salts such as Fe₃⁺ in oxidation reactions.
Palladium (Pd) compounds in pharmaceutical manufacturing reactions.

## Slide 8
✖ Difficulty in separating the catalyst from the products, making reuse expensive.
✖ Environmental problems if the catalyst is toxic or requires organic solvents.
✖ Higher purification costs.
✔ Very high selectivity: It yields precisely defined products, which is beneficial in the pharmaceutical industry.
✔ Fast and homogeneous reaction: because the catalyst is completely mixed with the reactants.
✔ Easier reaction control: such as by changing the pH or the concentrations of the substances
Advantages:
Disadvantages:

## Slide 9
2. Heterogeneous CatalysisIn
this type of catalysis, the catalyst is in a different phase than the reactants.
Typically :
The catalyst is solid.
The reactants are gaseous or liquid.
A well-known example:
The solid nickel (Ni) catalyst used to convert liquid oils into margarine (hydrogenation).
Examples of heterogeneous catalysis:
Platinum (Pt) in automotive catalytic converters (for gas purification).
Iron (Fe) in the Haber process for ammonia production.
Zeolite catalysts in oil refining.
Nickel (Ni) in oil hydrogenation.

## Slide 10
Advantages:
Disadvantages:
✔ Easy to separate and reuse: The catalyst remains as a solid that can be filtered and separated.
✔ Suitable for large-scale industries: such as petrochemicals, where equipment operates for extended periods.
✔ Withstands high temperatures.
✔ Produces less waste.
✖ Less selective compared to homogeneous catalysis.
✖ May be susceptible to catalyst poisoning due to certain impurities.
✖ Sometimes requires high temperatures and pressures.

## Slide 11
3. Biocatalysis
This is the use of enzymes or microorganisms (bacteria, yeasts, etc.) as catalysts to accelerate reactions.
This type is the most environmentally friendly because:
It works in water
At low temperatures
And under very moderate conditions
Examples of biocatalysis:
Lipase enzyme in the manufacture of pharmaceuticals and aromatics.
Saccharomyces cerevisiae yeast in the fermentation of sugar to produce ethanol.
Catalase enzyme for breaking down hydrogen peroxide.
Bacteria for converting methane or CO2 into useful products.

## Slide 12
Advantages:
Disadvantages:
✔ Higher selectivity than all other types of catalysis (an enzyme can select one molecule over another with incredible precision).
✔ Does not use toxic solvents.
✔ Saves energy because it operates at temperatures between 20°C and 40°C.
✔ Biodegradable and non-polluting.
✖ Enzymes are sensitive to high heat or pH.
✖ High cost in some industrial applications.
✖ Difficulty maintaining the activity of the organisms for extended periods.

## Slide 13: Role of Catalysis in Sustainable Chemistry
03

## Slide 14
Catalysis plays a fundamental role in sustainable chemistry because it enables the transformation of reaction pathways from high-energy, non-selective routes to low-energy and highly selective alternatives. A catalyst reduces the activation energy without being consumed, allowing reactions to proceed under lower temperature and pressure conditions. This results in reduced energy consumption, improved atom-economy, and minimized formation of unwanted by-products.
examples:
1-CO₂ Hydrogenation to Methanol (CO₂ → CH₃OH)
Copper-based catalysts (Cu/ZnO/Al₂O₃) efficiently convert carbon dioxide into methanol under mild conditions—an example of carbon recycling and emission reduction.
2-Selective Oxidation Using Noble Metal Catalysts
Platinum or ruthenium catalysts can oxidize alcohols to aldehydes or ketones without using toxic oxidizing agents such as chromium(VI) compounds.

## Slide 15
3-Heterogeneous Catalysis in Petrochemical Refining
Zeolite catalysts in catalytic cracking improve fuel yield while lowering the required reaction energy.
4-Biocatalysis Using Enzymes
Enzymes like lipases catalyze esterification reactions to produce bio-esters in aqueous media, eliminating the need for hazardous organic solvents.
5-Hydrogen Production via Water Electrolysis
Nickel- or iridium-based catalysts reduce the energy needed for hydrogen evolution reactions, enabling more sustainable green hydrogen technologies.

## Slide 16: 04
Industrial application of Catalysis

## Slide 17
Catalysis plays a central role in a wide range of industrial sectors, as it enables faster
cleaner, and more energy-efficient chemical transformations. Modern
industries rely on catalytic processes to increase product yield, improve selectivity,
and reduce environmental impact.
1.Petrochemical Industry :
Catalysts are essential in refining crude oil.
• Catalytic cracking: Zeolite catalysts convert heavy hydrocarbons into lighter fuels such as gasoline.
• Hydrocracking: Metal catalysts (Ni, Mo, Pt) help produce high-quality fuels under controlled conditions.These processes improve fuel quality while reducing energy consumption.
2. Ammonia Production – Haber–Bosch Process :
• Iron-based heterogeneous catalysts enable the large-scale synthesis of ammonia (NH₃) from nitrogen and hydrogen.
This process is vital for producing fertilizers and supporting global agriculture.

## Slide 18
3. Polymer Industry :
Catalysts are used to manufacture plastics and synthetic materials.
• Ziegler–Natta catalysts: used in producing polyethylene and polypropylene.
• Metallocene catalysts: allow precise control over polymer structure and properties.
4. Pharmaceutical Industry :
Catalysis is essential for synthesizing complex molecules with high purity.
• Homogeneous metal catalysts (Pd, Rh) are used in hydrogenation, coupling reactions, and oxidation processes.
• Enzymatic biocatalysis offers greener routes to drug manufacture
5. Environmental Applications :
Catalysts help reduce pollution and protect the environment.
• Automotive catalytic converters: Platinum, palladium, and rhodium convert toxic exhaust gases
(CO, NOₓ, hydrocarbons) into less harmful compounds.
• Wastewater treatment: Catalysts degrade organic pollutants under mild conditions.

## Slide 19: 05
Future prospects of catalysis in sustainable development

## Slide 20
Catalysis is expected to play a central role in the future of industry and environmental sustainability. As science and technology advance, the focus is shifting toward developing catalysts that are more efficient, cost-effective, and environmentally friendly. Future directions aim to enhance chemical processes, reduce emissions, and enable new pathways for green energy and carbon recycling
1. Development of More Sustainable Catalysts :
Future research will emphasize designing catalysts based on abundant and low-cost metals such as iron, nickel, and cobalt instead of expensive noble metals like platinum and rhodium.
This will reduce costs while enabling large-scale industrial applications.
2. Nanocatalysis (Nanotechnology in Catalysis) :
Nanotechnology will significantly improve catalytic performance:
• Increased surface area
• Higher selectivity
• Reduced material consumption
These advantages make industrial processes more efficient and resource-friendly

## Slide 21
3. Advanced Biocatalysis :
The use of enzymes and microorganisms will continue to expand, especially in pharmaceutical and food industries.
Advances in genetic engineering will allow the creation of new enzymes that are:
• More heat-resistant
• Capable of working under harsh conditions
• Highly efficient
This supports cleaner and more sustainable industrial processes.
4. CO₂ Conversion and Upcycling
Catalysis will play a major role in converting CO₂ into valuable products such as:
•Methanol
•Synthetic fuels
•Polymers
•Industrial chemicals
This is a key step toward a low-carbon and circular economy.

## Slide 22
5. Recyclable and Regenerable Catalysts
The future aims to develop catalysts that can be easily regenerated and reused without losing activity.
Smart catalysts may also be designed to adapt their properties during reactions to maximize efficiency.

## Slide 23: 06
Conclusion

## Slide 24
Catalysis is essential in sustainable chemistry because it accelerates chemical reactions while reducing energy use and waste. The main types of catalysis—homogeneous, heterogeneous, and biocatalysis—each play important roles in improving efficiency and selectivity in chemical processes.
Catalysis is widely used in key industries such as petroleum refining, ammonia production, polymer manufacturing, pharmaceuticals, environmental protection, and clean energy technologies like biodiesel and green hydrogen.
In the future, catalysis will continue to advance through nanotechnology, improved biocatalysts, CO₂ conversion, and AI-based catalyst design, enabling cleaner, more efficient, and more sustainable industrial processes.
In short, catalysis is a fundamental tool for achieving sustainable development and greener technologies.

## Slide 25
Thank you for listening