## Slide 1
Democratic and Popular Republic of Algeria
Ministry of Higher Education and Scientific Research
Abd El-Hafid Boussouf University - Mila
Faculty of Sciences & Technology
Department of Process Engineering
HSE in Industrial Installations – UED2.1
Week IV:
Workplace Risk Analysis Methods

## Slide 2: Learning Outcomes
By the end of this session, students will be able to:
Apply observation-based techniques to identify hazards in the workplace.
Construct and interpret a risk map (cartographie des risques).
Use a risk assessment matrix (severity × probability).
Perform a basic hazard identification exercise (case study).

## Slide 3: 1. Introduction to Workplace Risk Analysis
Risk analysis is a systematic approach used to detect, understand, and evaluate dangers present in an installation before they lead to an accident.
Why it matters in process engineering :
Reduces accident frequency and severity.
Improves equipment reliability.
Helps decision-making for preventive measures.
Required by ISO 45001 and industrial auditing systems.
Example:
At a chemical mixing unit, operators frequently climb stairs while carrying solvents. A risk analysis reveals:
→ risk of slipping, fall from height, chemical exposure, ergonomic strain.

## Slide 4
1I. Observation Techniques: Overview
Observation techniques focus on direct inspection of work situations to identify visible and hidden hazards.
تقنيات المراقبة
Planned Observation :
Structured visit using a checklist.
Spontaneous Observation :
Unscheduled visit during normal operations.
Task Analysis Observation :
Breakdown of tasks into steps to identify hazards.
Behavior-Based Safety Observation (BBS) :
Focus on worker behavior relative to safety standards.

## Slide 5
III. Risk Mapping
A risk map is a visual representation of all identified hazards in a workplace or industrial unit.
It provides:
Location of hazards (geographical or process-based).
Nature / type of hazards (chemical, mechanical, thermal…).
Risk level (coding with colors).
Priority zones for intervention.

## Slide 6
IV. How to Build a Risk Mapping
Step 1 – Identify the area
Define the boundaries of the zone (e.g., distillation unit, storage area).
Step 2 – Collect information
Using:
Site visits and observations
Accident history
Near miss reports
Worker interviews
Step 3 – Identify hazards
For each workplace: chemical, physical, mechanical, ergonomic, biological.
Step 4 – Assess risk level
(using the risk matrix introduced later).
Step 5 – Plot hazards on the map
Use icons, colors, or labels depending on severity.
Step 6 – Validate with HSE team and supervisors

## Slide 7
V. Risk Assessment Matrices
A risk assessment matrix combines the severity of consequences with the probability of occurrence.
The matrix cross-combines S and P to produce risk levels
(low / medium / high / critical).

## Slide 8
VI. Example: Risk Matrix Interpretation

## Slide 9
IIIX. Summary
Observation techniques allow direct detection of hazards.
Risk mapping visualizes location, nature, and intensity of hazards.
Risk matrices objectively classify risks to prioritize interventions.

## Slide 10
IIX. Next Session
Week 5: Accident Analysis – Introduction to Tree of Causes
Thank you for your attention!
See you next class.