## Slide 1: Power Plants
Chapter 1: Overview
How electricity is generated and delivered to the grid

## Slide 2: What is a power plant?
Power plant
Intended for electricity generation. It supplies electricity, via the power grid, to private and industrial consumers located far from the plant.
Electricity generation
A primary energy is converted into electrical energy. It can be mechanical, chemical, nuclear or solar.

## Slide 3: Classification by primary energy
Fossil fuels
Coal, fuel oil and natural gas, burned in boilers or gas turbines. Still the most widely used worldwide.
Other fuels
Biomass or household waste, burned in specific boilers.
Nuclear
Heat for steam comes from the fission of uranium.
Solar
Solar boilers producing steam for a turbine, or plants made of many photovoltaic panels.
Hydraulic
River currents or falling water (dams, penstocks) drive the turbine powering the alternator.
Wind
The force of the wind drives an alternator.

## Slide 4: Technologies and types of plants
By technology
Mechanical energy converted by alternators, driven by:
Hydraulic turbine
Wind turbine
Steam or gas turbine
Other sources: chemical energy (oil, gas, wood, waste) and nuclear energy.
Types of power plants
Nuclear
Hydroelectric
Flame thermal
Flameless thermal
Wind turbines
Photovoltaic

## Slide 5: The alternator and the transformer
Alternator
Converts mechanical energy into electricity. Used in every power plant, whatever the energy source. A rotor rotates inside a stator.
Example: 1300 MW, 1500 rpm, 50 Hz three-phase
Transformer
Adapts the voltage generated by the alternator before it is fed into the power grid.

## Slide 6: How power plants work
1
Steam or water sets the turbine in rotation. In a wind turbine, the wind turns a 3-blade propeller.
2
The rotating turbine turns the generator shaft.
3
In the alternator, the rotor (magnets) turns inside the stator (a fixed coil).
4
The alternator generates the electric current.

## Slide 7: World electricity production
62.5%
Flame thermal
Thermal power plants
17.5%
Nuclear
Thermal power plants
20%
Renewables
Hydroelectric, solar, geothermal, wind, tidal